## Slide 1
The Effect of Infill Parameters on Spatiotemporal Thermal Distribution in Fused Deposition Modeling
3D printing has grown into a widely explored technology in many industries, such as construction, aerospace, and medicine, because of its ability to rapidly produce prototypes.
For many of these industries, the thermal properties of products are crucial to functionality. Therefore, it is critical to understand specific factors that influence these thermal properties.
During the 3D printing process, thermal stresses creates distortions, known as warpage. Limited research has been done on solutions to the warpage problem in FDM printing.
This study aims to understand the relationship between infill parameters and the spatiotemporal temperature distribution during the printing process.
PURPOSE
Table 2: Sample Section of Raw Data from 20% Infill Print
Fused deposition modeling (FDM) is the most popular method for 3D printing due to its low production costs. In FDM, a thermoplastic filament is melted and extruded onto a surface repeatedly to produce a 3D object.
Warpage occurs as cycles of heating and cooling layers cause thermal stresses of expansion and contraction.
Plastic is used as filament in 3D printing. The discontinuous atomic nature of plastic causes its heat properties to be anisotropic and influenced by the internal structure, or infill.
Infill percentage refers to the proportion of plastic in an 3D printed object.
Current research on this topic fails to account for environmental factors as well as failing to consider factors that affect thermal properties.
Figure 1: Warpage in 3D printing
3dprinting.com/tips-tricks/how-to-choose-an-infill-for-your-3d-prints
BACKGROUND
Greater infill percentages will have more uniform distributions of temperature because conduction has been shown to be more effective than radiation or convection for heat transfer in enclosed structures.
IV: Infill percentage (10%, 20%, 30%)
DV: Temperature at specific points over time
HYPOTHESIS
Figure 2: Various Infill Percentages
tcadsolutions.com/3dprinting.html
EXPERIMENTAL DESIGN
DATA
Sliced the model three times using a rectilinear infill pattern with 10%, 20%, and 30% infill percentage
RESULTS
At any time t, the entire system is at a steady state temperature since the rate of heat flow into the system is the rate of heat flow out of the system. Therefore, it can be modeled by Fourier’s Law of Heat Conduction, where is the heat flux density, k is the thermal conductivity, and is the temperature gradient:
Since the system at any time is at a steady-state, and the temperature gradient is directly proportional to the heat flux density, the center of temperature distribution can be found similarly to finding the center of mass assuming linear masses. In this system, each point can be assigned a “weight” that represents its temperature. The center can then be calculated by finding the weighted mean in the horizontal (x) and vertical (y) distances:
Center of Temperature = ( , )
When all temperatures are equal to each other, the center of temperature represents a common equilibrium point for when the entire system is at a perfect steady-state thermal equilibrium, and the weighted mean can be calculated with all weights equal:
Equilibrium Point = (5.175, 10.525)
For each calculated center, the weighted mean of the temperature was also calculated:
where r is the distance from the center to the equilibrium point. The horizontal and vertical components of the gradient vector were also calculated for each center from the equilibrium point to find the magnitude and direction of net temperature change:
A Welch’s Test was run on the resultant gradients for each infill:
RESULTS
The Welch’s Tests showed that the mean gradients for the 30% infill were significantly greater (p<0.0001) than the mean gradients for 20% infill. Additionally, the mean gradients for the 20% infill were also significantly greater (p<0.0001) than the mean gradients for the 10% infill. Therefore, this data suggests that as infill percentage increases, the mean gradient from equilibrium also increases, and since the gradient is directly proportional to the heat flux density as per Fourier’s Law, the net heat flow also increased.
This can be explained because theoretically, thermal conductivity increases with infill percentage since there is more plastic.
Therefore, this experiment’s data supported the hypothesis.
CONCLUSIONS
The conclusions in this study are based on limited data, and repeating this experiment with multiple trials of each infill would reduce the variability of data for each point and allow for more accurate generalizations of a relationship.
More infill percentages can also be printed to investigate whether the suggested relationship is maintained. Other parameters can also be considered, such as infill pattern and filament material or color.
As temperature is a scalar function, to actually be able to accurately analyze the temperature gradients in this experiment, the function must be known. Future research on finding this function using scattered, discrete temperature values can be conducted, such as by using Deep Learning models like Artificial Neural Networks to produce mapping functions for the data.
FUTURE WORK
Designed CAD model of an 8-inch diameter, 0.5 inch thick disc with 14mm wide channels
Print the sliced model on the gCreate gMax 1.5XT+ with PLA and print settings in Table 1
Embed 8 NTC thermistors into the channels and record data using an Arduino Voltage Circuit and puTTY
Figure 3: CAD Model of Template Disc
Figure 4: Embedding Thermistors during Printing
Table 1: Printer Settings for All Prints. Settings not mentioned were left as the default values.
Setting | Value
Extruder Temperature | 200°C
Bed Temperature | 80°C
Layer Height | 0.2 mm
Time (seconds) | Thermistor 1 (°C) | Thermistor 2 (°C) | Thermistor 3 (°C) | Thermistor 4 (°C) | Thermistor 5 (°C) | Thermistor 6 (°C) | Thermistor 7 (°C) | Thermistor 8 (°C)
618 | 31.93 | 30.48 | 28.34 | 29.41 | 24.36 | 26.66 | 24.46 | 26.26
619 | 31.84 | 30.09 | 28.14 | 29.31 | 24.36 | 26.66 | 24.56 | 26.36
620 | 31.84 | 29.7 | 27.94 | 29.31 | 24.46 | 26.56 | 24.46 | 26.36
621 | 31.84 | 29.41 | 27.75 | 29.22 | 24.56 | 26.56 | 24.46 | 26.36
622 | 31.84 | 29.12 | 27.65 | 29.31 | 24.66 | 26.46 | 24.46 | 26.36
623 | 31.84 | 28.92 | 27.55 | 29.31 | 24.56 | 26.46 | 24.36 | 26.36
624 | 31.84 | 28.63 | 27.55 | 29.61 | 24.66 | 26.36 | 24.36 | 26.36
10% and 20% infills | 
Test Statistic | -34.9745
p-value (two-tailed) | <0.0001
p-value (one-tailed) | <0.0001
20% and 30% infills | 
Test Statistic | -8.4609
p-value (two-tailed) | < 0.0001
p-value (one-tailed) | < 0.0001
Figure 6: 20% Infill Temperature Centers, STDx = 1.40, STDy = 0.94
Figure 5: 10% Infill Temperature Centers, STDx = 0.87, STDy = 0.59
Figure 7: 30% Infill Temperature Centers, STDx = 0.87, STDy = 0.64