## Slide 1: Effect of infill parameters on spatial temperature distribution in fused deposition modeling
Pranav Addepalli

## Slide 2: Significance
Warpage
Passive heating
Crucial for future 3D printing
  Aerospace and defense, automotive, and healthcare
https://3dprinting.com/tips-tricks/how-to-choose-an-infill-for-your-3d-prints/
http://www.3dprinterworld.com/article/3d-printing-enables-university-students-become-aerospace-manufacturers

## Slide 3: My Project
Studying the effect that various infill combinations have on
thermal conductivity
spatial temperature distribution
in PLA discs during the printing process.
https://www.dddrop.com/wp-content/uploads/2018/02/3D-printen-stevige-infill.jpg

## Slide 4: Variables
Infill type and infill percentage
Temperature distribution and thermal conductivity
http://tcadsolutions.com/3dprinting.html
https://3dprinting.com/tips-tricks/how-to-choose-an-infill-for-your-3d-prints/

## Slide 5: Hypothesis
Conduction in porous structures is superior to radiation and natural convection
  (Deng et. al., 2018; Larkin & Churchill, 1959; Kim & Viskanta, 1984)
Higher infill percentages will have higher thermal conductivities
  Higher infill percentage  more plastic  more conduction
Hexagonal infill will have the highest thermal conductivity
  Hexagons have the most “channels”  more pathways for heat flow

## Slide 6: Materials
Thermistors
PLA
Arduino Uno R3
Lees’ Disc
https://www.mouser.com/ProductDetail/Amphenol-Advanced-Sensors/TH420J34GDNI?qs=P8zB4ONU6fzOyUXxdGay3g%3D%3D

## Slide 7: Procedure
Use Fusion360 to design a template disc with 8 inch diameter, 0.5 inch height, and channels for thermistors
Slice the disc in Cura with a different infill each time
  Hexagonal, rectilinear, triangular
  10%, 20%, 30%, 40%, 50%
  3 trials of each infill combination

## Slide 8: Procedure: Lees’ Disc
Construct a Lee’s Disc Apparatus
Brass, steam generator, and steam chamber
http://pubs.sciepub.com/ajme/2/4/3/figure/2

## Slide 9: Procedure: Recording Data
Program Arduino to record time-temperature data with the Steinhart-Hart Equation
  Finds temperature based on resistance and other values constant to thermistor type
http://blog.skytee.com/2012/01/temperature-sensor/

## Slide 10: Progress

## Slide 11: Disc Template
Randomly selected positions along 1 inch increments
7mm channels

## Slide 12: Lees’ Disc Apparatus
Presented to Monroe and began collaboration
  Aluminum cylinder and brass discs delivered last week to Welding students
  Capping the cylinder and drilling in/out holes to make a steam tank
Started assembling the apparatus
  Drilling holes in the brass to hang up and for temperature probes

## Slide 13: Thermistors (1)
Tested for coefficients
Constructed a temperature and resistance curve specific to the model

## Slide 14: Thermistors (2)
Programmed and wired the Arduino to record several temperatures in Serial
Sample temperature distribution for 4 thermistors
Taped circuit connections for insertion in the print

## Slide 16: Simulation
Looking for CFD software to run thermal analyses on each model
New engineering research PC?

## Slide 17: Future Goals
Finish the Lees’ Disc Apparatus and test
Simulations
Main issue: no working 3D printers big enough
  Need a printer with a bed at least 8.5 x 8.5 inches, but the Series 1 Pro that we have is broken
  Ordered a new 3D printer (Raise3D Pro2) with a 12” x 12” x 11.8” build space

## Slide 18: References
Deng, C., Kang, J., Shangguan, H., Hu, Y., Huang, T., Liu, Z. (2018). Effects of hollow structures in sand mold manufactured using 3D printing technology. Journal of Materials Processing Technology, 255, 516-523. doi:10.1016/j.jmatprotec.2017.12.031
Larkin, B. K. & Churchill, S. W. (1959). Heat transfer by radiation through porous insulations. AIChE Journal, 5(4), 467-474. doi:10.1002/aic.690050413
Kim, D. M. & Viskanta, R. (1984). Heat transfer by conduction, natural convection, and radiation across a rectangular cellular structure. International Journal of Heat & Fluid Flow, 5, 205-213. doi:10.1016/0142-727X(84)90053-5